Headwaters Compactor Site
Headwaters, Va.
BIDS FOR Headwaters Compactor Site
SCOPE OF WORK
Highland County is seeking a contractor to complete concrete and grading work located at the solid waste compactor site in Headwaters. This includes but is not limited to site improvement, grading, concrete forming, pouring, welding and removal of dirt. (Please see attached bid sheet for full scope of work).
Contractor will provide all labor, supervision, equipment, tools, materials, and incidentals to complete the work. The contractor will work with Alleghany Disposal, LLC., for site improvement to accommodate the new compactor equipment.

QUALIFICATIONS OF BIDDERS AND BIDDING PROCESS:
Bids must be placed in a sealed envelope with “HEADWATERS SITE” written on the front of the envelope. Bids are due June 1, 2025
Bids may be submitted to Jerri Botkin, County Administrator’s Office at the Courthouse (P. O. Box 130, Monterey, VA)
The attached BID Sheet must be completed in its entirety in order to be considered.
The successful bidder shall purchase and maintain such liability and other insurance as is appropriate for the work being performed including worker’s compensation insurance and shall provide the county with Certificates of Insurance.
Highland County reserves the right to reject any or all bids in whole or in part and to waive any irregularities or informalities in the bidding.

HIGHLAND COUNTY BOARD OF SUPERVISORS
BID SHEET
PROJECT: Headwaters Compactor Site
Contractor Name: _______________________________________
Contact Information: _____________________________________
Date: __________________________
Item No.	Description	Quantity / Size	Unit Price ($) / Inclusive of all labor, profit, and overhead	Total Price ($)
1	Demolition of partial 10’ by 24’ existing slab	Lump Sum
2	Excavation of area for additional pad length-material must be hauled off site
3	Digging of footers-6” of gravel
4	Grass seed and straw placed on all excavated areas
5	Concrete footers totaling 80’ lineal foot 3’ width, 8” thick, reinforced and poured with a 3,000-psi mix	80 lineal feet
6	Retaining wall (8' H x 8" thick, 4,000 PSI, match brick form)	58 linear feet
7	Concrete curbs 80’ lineal feet by 2’ width 4,000PSI **curbs must be 8” above slab elevation	80 linear feet
8	Concrete pad (13' 6" x 52', 8" thick, 4,000 PSI) broom finish	713sq. ft. (approx.)
9	Welding-24” high expanded handrail to be installed on 8’ concrete wall on ramp side
10	Modifications to factory supplied compactor chute to attach the chute to retaining wall
	Total

Notes:
- All concrete work to be reinforced and conform to listed PSI standards.
- Brick form on the retaining wall must match existing for aesthetic continuity.
- Contractor is responsible for all labor, equipment, materials, permits, and site cleanup.
- There will be no change in orders accepted after the bid is accepted.
- The selected bidder will work with Allegheny Disposal, L.L.C. for site improvement to accommodate new compactor equipment